## Slide 1: Yakima RM 153 Side Channel Implementation
Project 26-1647
Kittitas County Conservation District

## Slide 2: Background
  Project Assessment and Design Completed in 2018 (Project 15-1147)
    Led by Trout Unlimited Washington Water Project
    Design Engineers: Herrera Environmental Consultants
  Construction not pursued
  December 2025 and February 2026
  flood events

## Slide 3: Yakima RM 153 Side Channel Implementation
The project site is in the Upper Yakima River watershed in Kittitas County, immediately south of Ellensburg.

## Slide 4: Yakima RM 153 Side Channel Implementation
The project site is located along the Yakima River’s west bank between river miles 151.7 – 153.0

## Slide 5: Yakima RM 153 Side Channel Implementation

## Slide 6: Adult and Juvenile Timing
Species (Adult/Juvenile) | Jan | Feb | Mar | Apr | May | Jun | Jul | Aug | Sep | Oct | Nov | Dec
Westslope Cutthroat (A/J) |  |  |  |  |  |  |  |  |  |  |  | 
Resident O. mykiss (A/J) |  |  |  |  |  |  |  |  |  |  |  | 
Sockeye (A) |  |  |  |  |  |  |  |  |  |  |  | 
Sockeye (J) |  |  |  | • | • | • |  |  |  |  |  | 
Summer steelhead (A) |  |  |  |  |  |  |  |  |  |  |  | 
Summer steelhead (J) |  |  | • | • | • | • |  |  |  |  |  | 
Spring Chinook (A) |  |  |  |  |  |  |  |  |  |  |  | 
Spring Chinook (J) |  |  | • | • | • | • |  |  |  |  |  | 
Coho (A) |  |  |  |  |  |  |  |  |  |  |  | 
Coho (J) |  |  | • | • | • | • |  |  |  |  |  | 
Denotes outmigration period

## Slide 7: Design Development by TU
Design project aimed to improve natural river processes, enhance fish habitat, and address past ecological damage while supporting agriculture of the Kittitas Valley.
Key problems:
  Levees: Two levees on the project site restrict the river's natural interaction with the floodplain, leading to channel incision, coarser bed material, and reduced side-channel habitat for salmonids. ​
  Spring Channels: Historical irrigation and land use have degraded small spring channels, creating barriers like culverts and irrigation structures that block fish passage. ​ Juvenile salmonids use these channels seasonally but face risks of stranding and mortality due to disconnection during low flows. ​
  Unnatural Pond: A former gravel pit pond receives river inflows at high flows, allowing juvenile salmonids to enter but often stranding them when flows drop. ​ This exposes them to predation and poor water quality.

## Slide 8: Levee Photos (courtesy of TU)

## Slide 9: Spring Channels (photos courtesy of TU)
Year-round flow, higher in summer
Over 2000’ on the property
Culverts and irrigation structures restrict access
Established riparian forest protects about 800’
Minimal fish presence

## Slide 10: Passage Barriers (photos courtesy of TU)

## Slide 11: Design Development
Technical Advisory Group
  National Marine Fisheries Service
  U.S. Fish and Wildlife Service
  U.S. Bureau of Reclamation
  Washington Department of Fish and Wildlife
  Washington Department of Ecology
  Kittitas County Conservation District
  Mid-Columbia Fisheries Enhancement Group
  Washington Department of Natural Resources
  Washington Department of Transportation
  Yakama Nation.

## Slide 20: Limitations and Constraints
Property owner may want changes in the design and/or have different goals
  Meeting April 16, 2026; Participation in Site Visit
Erosion of the levee adjacent to the property may necessitate redesign work which could need involvement of a geotechnical engineer and a surveyor to update the site topo and increase costs
  Utilize Emergency Watershed Protection (EWP) Program funding for at least upper end of Jensen Levee site conditions update; Seeking immediate additional funding for site evaluation of entire levee area and for construction
  Reconvene Technical Work Group to review project